## Slide 2: Contents
Packet over SONET(POS)
    Architecture and Operation
    Advantages of PoS
    Applications
ADSL (Asymmetric Digital Subscriber Line)
    Difference between ADLS and SDLS
Data Over Cable Service Interface Specification (DOCSIS)
    DOCSIS Architecture
    Versions of DOCSIS
    Features of DOSCIS

## Slide 3: Packet over SONET
Packet over SONET (PoS) is a technology applied in the communication industry to send packets, typically IP packets, through the SONET (Synchronous Optical Network) or SDH (Synchronous Digital Hierarchy).
They are heavily used by telecommunication networks because of their high speed, reliability and ability to handle large amount of data.
SONET and SDH are two internationally standardized protocols used for transmitting information on optical fiber networks
These protocols allow long distance digital transmissions with minimum loss and highest reliability
. In North America, SONET is commonly applied during network design while SDH is used for the other parts of the world.

## Slide 4: Architecture and Operation
PoS architecture involves packetizing packets in order to transmit them across the SONET/SDH network. Some important components include:
Encapsulation: The process of encapsulation entails adding headers and trailers to the packets in order to make them suitable for transmission on a network.
For this purpose, there are two primary protocols used:
Point-to-Point Protocol (PPP): In PoS, PPP is frequently employed for packet encapsulation. It offers a standard means of conveying multiprotocol datagrams across point-to-point links.
High-Level Data Link Control (HDLC): HDLC is one more possible protocol employed within PoS for encapsulation purposes.
2. SONET/SDH Framework: These encapsulated packets are then transmitted over the SONET/SDH network. Hierarchical structure is designed in such a way as to divide SONET/SDH networks into several layers each with its own specific functions:
Physical Layer: This is made up of optical fibers as well as associated hardware that receives or sends optical signals.
Section Layer: Responsible for physical transmission of signal over fiber including framing errors and correction.
Line Layer: Ensures the reliable transfer of data across the network by managing synchronization, multiplexing, and demultiplexing.
Path Layer: Handles the end-to-end transport of data, ensuring that packets are correctly routed and delivered to their destination.

## Slide 5: Advantages of Packet over SONET
High Bandwidth
Reliability
Scalability
Interoperability

## Slide 6: Applications
Backbone Network :In backbone networks, PoS is utilized to attach major network nodes, could high-speed, reliable data transmission be tunneling over long distances. These are standard and traditional LANs and WANs that are at the heart of the internet and large organizations data networks.
Metropolitan Area Networks (MANs) : MANs also use PoS as a means of connecting several LANs in a city or a region it serves. This allows the network to deliver high speed data links connecting up different regions in a metropolitan area with applications like video conferencing, data mirroring and backup, and disaster recovery.
Carrier Ethernet Services : Carrier Ethernet services rely on the PoS’s in depth involvement, assisting business customers in attaining high speed, stable connectivity.
Data centers and cloud services : When it comes to the data centers and cloud services, PoS is employed for connecting the servers and storage systems, with fast and efficient transfer rates.

## Slide 7: ADSL (Asymmetric Digital Subscriber Line)
Digital subscriber lines (DSLs) are high-speed Internet connections that use standard telephone lines.
DSL uses the standard twisted-pair telephone lines that come into every home for normal telephone service.
The main selling point of DSL is widespread availability.
ADSL (Asymmetric Digital Subscriber Line) is a technology that facilitates fast data transmission at a high bandwidth on existing copper wire telephone lines to homes and businesses.
ADSL is asymmetric in that it uses most channels to transmit downstream to the user and only a small part for uploading information from the user.

## Slide 8: Con’t
ADSL simultaneously accommodates analog (voice) information and data on the same phone line. It is generally offered at downstream internet connection data rates from 512 kilobits per second (Kbps) to about 6 megabits per second (Mbps).
It works on the principle that since voice does not use anything like all of the bandwidth available from a standard copper twisted pair line, it’s possible to maintain a high-speed data connection at the same time.
ADSL works on existing copper phone lines by using a DSL filter, or splitter, to isolate the bands with higher frequencies so that the landline and the ADSL modem can be used at the same time.
At the central office, or telephone exchange, the line ends at the DSL access multiplexer (DSLAM), where an additional splitter segregates the voice signal to the phone network.
It was designed to exploit the one-way nature of most multimedia communication in which large amounts of information flow toward the user and only a small amount of interactive control information is returned.

## Slide 9: How does ADSL differ from SDSL?
The most major difference between these two groups is in how much bandwidth they allocate to the user.
Since SDSL is symmetric , It offers equal download and upload speeds to the user while, although the download speed is also very high for ADSL, the upload speed can be significantly slower.
Some people, especially those who upload videos or other content, may prefer the high upload bandwidth of SDSL, but for most people, ADSL provides sufficient upload speed since we download much more information than we upload while browsing the internet, watching videos, and downloading files.
ADSL is a standardized technology and as such, most devices that can operate with ADSL can be used interchangeably , they adapt to the standard and are therefore compatible.
SDSL is proprietary and was never standardized, leaving manufacturers to implement their own standards in how their devices are supposed to operate.

## Slide 10: Data Over Cable Service Interface Specification (DOCSIS)
DOCSIS is a telecommunications standard used globally to provide high-speed internet access via cable TV networks.
This technology enables continuous connection with the internet over cable by converting data to a format easily transmitted over these networks.
This technology enables continuous connection with the internet over cable by converting data to a format easily transmitted over these networks.
The purpose of DOCSIS is to help cable providers deliver high-speed broadband internet service to their customers, over their existing hybrid fiber coaxial infrastructure, without the need for substantial renovations of the existing network.
DOCSIS is utilized predominantly for transferring data over the internet to our homes, places of work, or wherever we connect digitally.

## Slide 11: DOCSIS Architecture
The DOCSIS architecture consists of two primary components :
A cable modem located with the customer and
the cable modem termination system operated by cable service providers
The second function is to perform as a Hi-Speed way station for multiple cable modems and then communicate with the system network.
DOCSIS defines protocol for bi-directional signal exchange between these two components through the use of cable.

## Slide 12: Versions of DOCSIS
DOSCIS 1.0 − It was the first version for cable modem system.
DOSCIS 2.0 − It enhanced upstream data from computer to the operator to allow services requiring equal data transfer in both uplink and downlink, like IP telephony.
DOSCIS 3.0 − It supports IPv6 standard. It is marked by increase in transmission speed for both uplink and downlink.
DOSCIS 3.1 Full Duplex − It uses full cable spectrum simultaneously for both uplink and downlink data transfer.

## Slide 13: Features of DOSCIS
Downstream data rate is typically 6MHz. Upstream data rate is up to 3.2MHz for DOCSIS 1.0 and 6.4MHz for later versions.
For simultaneous multiple transmissions, time division multiple access (TDMA) and code division multiple access (CDMA) are used.
It supports channel bonding that allows a subscriber to use multiple downstream and upstream channels simultaneously.
It supports applications requiring low latency like Voice over IP.
DOCSIS modems are managed by IP addresses. DOCSIS 3.0 and above supports IPv6.

## Slide 14: THANK YOU FOR PAY ATTENTION